## Slide 1: CHAPTER 13 GAS MIXTURES
Lecture slides by
Mehmet Kanoglu
Copyright © The McGraw-Hill Education. Permission required for reproduction or display.
Thermodynamics: An Engineering Approach
8th Edition Yunus A. Çengel, Michael A. Boles
McGraw-Hill, 2015

## Slide 2
Objectives
Develop rules for determining nonreacting gas mixture properties from knowledge of mixture composition and the properties of the individual components.
Define the quantities used to describe the composition of a mixture, such as mass fraction, mole fraction, and volume fraction.
Apply the rules for determining mixture properties to ideal-gas mixtures and real-gas mixtures.
Predict the P-v-T behavior of gas mixtures based on Dalton’s law of additive pressures and Amagat’s law of additive volumes.

## Slide 3
COMPOSITION OF A GAS MIXTURE: MASS AND MOLE FRACTIONS
To determine the properties of a mixture, we need to know the composition of the mixture as well as the properties of the individual components. There are two ways to describe the composition of a mixture:
Mass fraction
Mole fraction
Molar analysis: specifying the number of moles of each component
Gravimetric analysis: specifying the mass of each component

## Slide 4
Apparent (or average) molar mass
Gas constant
The molar mass of a mixture
Mass and mole fractions of a mixture are related by
The sum of the mass and mole fractions of a mixture is equal to 1.

## Slide 5
P-v-T BEHAVIOR OF GAS MIXTURES: IDEAL AND REAL GASES
The prediction of the P-v-T behavior of gas mixtures is usually based on two models:
Dalton’s law of additive pressures: The pressure of a gas mixture is equal to the sum of the pressures each gas would exert if it existed alone at the mixture temperature and volume.
Amagat’s law of additive volumes: The volume of a gas mixture is equal to the sum of the volumes each gas would occupy if it existed alone at the mixture temperature and pressure.

## Slide 6
For ideal gases, Dalton’s and Amagad’s laws are identical and give identical results.
Pi component pressure Vi component volume
Pi /Pm pressure fraction Vi /Vm volume fraction

## Slide 7
Ideal-Gas Mixtures
This equation is only valid for ideal-gas mixtures as it is derived by assuming ideal-gas behavior for the gas mixture and each of its components.
The quantity yiPm is called the partial pressure (identical to the component pressure for ideal gases), and the quantity yiVm is called the partial volume (identical to the component volume for ideal gases).
Note that for an ideal-gas mixture, the mole fraction, the pressure fraction, and the volume fraction of a component are identical.
The composition of an ideal-gas mixture (such as the exhaust gases leaving a combustion chamber) is frequently determined by a volumetric analysis (Orsat Analysis).

## Slide 8
Real-Gas Mixtures
Zm is determined by using these pseudocritical properties.
The result by Kay’s rule is accurate to within about 10% over a wide range of temperatures and pressures.
Kay’s rule
Zi is determined either at Tm and Vm Dalton’s law) or at Tm and Pm (Amagat’s law) for each individual gas. Using Dalton’s law gives more accurate results.
Compressibility factor

## Slide 9
PROPERTIES OF GAS MIXTURES:
IDEAL AND REAL GASES
Extensive properties of a gas mixture
Changes in properties of a gas mixture

## Slide 10
Extensive properties of a gas mixture
Properties per unit mass involve mass fractions (mfi) and properties per unit mole involve mole fractions (yi).
The relations are exact for ideal-gas mixtures, and approximate for real-gas mixtures.

## Slide 11
Ideal-Gas Mixtures
Gibbs–Dalton law: Under the ideal-gas approximation, the properties of a gas are not influenced by the presence of other gases, and each gas component in the mixture behaves as if it exists alone at the mixture temperature Tm and mixture volume Vm.
Also, the h, u, cv, and cp of an ideal gas depend on temperature only and are independent of the pressure or the volume of the ideal-gas mixture.

## Slide 12
Real-Gas Mixtures
This equation suggests that the generalized property relations and charts for real gases developed in Chap. 12 can also be used for the components of real-gas mixtures. But TR and PR for each component should be evaluated using Tm and Pm.
If the Vm and Tm are specified instead of Pm and Tm, evaluate Pm using Dalton’s law of additive pressures.
Another way is to treat the mixture as a pseudopure substance having pseudocritical properties, determined in terms of the critical properties of the component gases by using Kay’s rule.
T ds relation for a gas mixture

## Slide 13: Summary
Composition of a gas mixture: Mass and mole fractions
P-v-T behavior of gas mixtures
  Ideal-gas mixtures
  Real-gas mixtures
Properties of gas mixtures
  Ideal-gas mixtures
  Real-gas mixtures