## Slide 1: CHAPTER 3 PROPERTIES OF PURE SUBSTANCES
Lecture slides by
Mehmet Kanoglu
Copyright © The McGraw-Hill Education. Permission required for reproduction or display.
Thermodynamics: An Engineering Approach
8th Edition Yunus A. Çengel, Michael A. Boles
McGraw-Hill, 2015

## Slide 2
Objectives
Introduce the concept of a pure substance.
Discuss the physics of phase-change processes.
Illustrate the P-v, T-v, and P-T property diagrams and P-v-T surfaces of pure substances.
Demonstrate the procedures for determining thermodynamic properties of pure substances from tables of property data.
Describe the hypothetical substance “ideal gas” and the ideal-gas equation of state.
Apply the ideal-gas equation of state in the solution of typical problems.
Introduce the compressibility factor, which accounts for the deviation of real gases from ideal-gas behavior.
Present some of the best-known equations of state.

## Slide 3: PURE SUBSTANCE
Pure substance: A substance that has a fixed chemical composition throughout.
Air is a mixture of several gases, but it is considered to be a pure substance.

## Slide 4: PHASES OF A PURE SUBSTANCE
The molecules in a solid are kept at their positions by the large springlike inter-molecular forces.

## Slide 5: PHASE-CHANGE PROCESSES OF PURE SUBSTANCES
Saturated liquid: A liquid that is about to vaporize
Compressed liquid (subcooled liquid): A substance that it is not about to vaporize

## Slide 6
Saturated vapor: A vapor that is about to condense.
Saturated liquid–vapor mixture: The state at which the liquid and vapor phases coexist in equilibrium.
Superheated vapor: A vapor that is not about to condense (i.e., not a saturated vapor).
As more heat is transferred, part of the saturated liquid vaporizes (saturated liquid–vapor mixture).
At 1 atm pressure, the temperature remains constant at 100°C until the last drop of liquid is vaporized (saturated vapor).
As more heat is transferred, the temperature of the vapor starts to rise (superheated vapor).

## Slide 7
T-v diagram for the heating process of water at constant pressure.
If the entire process between state 1 and 5 is reversed by cooling the water while maintaining the pressure at the same value, the water will go back to state 1, retracing the same path, and in so doing, the amount of heat released will exactly match the amount of heat added during the heating process.

## Slide 8: Saturation Temperature and Saturation Pressure
The temperature at which water starts boiling depends on the pressure; therefore, if the pressure is fixed, so is the boiling temperature.
Water boils at 100C at 1 atm pressure.
The liquid–vapor saturation curve of a pure substance (numerical values are for water).
Saturation temperature Tsat: The temperature at which a pure substance changes phase at a given pressure.
Saturation pressure Psat: The pressure at which a pure substance changes phase at a given temperature.

## Slide 9
Latent heat: The amount of energy absorbed or released during a phase-change process.
Latent heat of fusion: The amount of energy absorbed during melting. It is equivalent to the amount of energy released during freezing.
Latent heat of vaporization: The amount of energy absorbed during vaporization and it is equivalent to the energy released during condensation.
The magnitudes of the latent heats depend on the temperature or pressure at which the phase change occurs.
At 1 atm pressure, the latent heat of fusion of water is 333.7 kJ/kg and the latent heat of vaporization is 2256.5 kJ/kg.
The atmospheric pressure, and thus the boiling temperature of water, decreases with elevation.

## Slide 10: Some Consequences of Tsat and Psat Dependence
The variation of the temperature of fruits and vegetables with pressure during vacuum cooling from 25°C to 0°C.
In 1775, ice was made by evacuating the air space in a water tank.

## Slide 11: PROPERTY DIAGRAMS FOR PHASE-CHANGE PROCESSES
The variations of properties during phase-change processes are best studied and understood with the help of property diagrams such as the T-v, P-v, and P-T diagrams for pure substances.
T-v diagram of constant-pressure phase-change processes of a pure substance at various pressures (numerical values are for water).

## Slide 12
saturated liquid line
saturated vapor line
compressed liquid region
superheated vapor region
saturated liquid–vapor mixture region (wet region)
At supercritical pressures (P > Pcr), there is no distinct phase-change (boiling) process.
Critical point: The point at which the saturated liquid and saturated vapor states are identical.

## Slide 14: Extending the Diagrams to Include the Solid Phase
At triple-point pressure and temperature, a substance exists in three phases in equilibrium.
For water,
Ttp = 0.01°C
Ptp = 0.6117 kPa

## Slide 15
Sublimation: Passing from the solid phase directly into the vapor phase.
At low pressures (below the triple-point value), solids evaporate without melting first (sublimation).
P-T diagram of pure substances.
Phase Diagram

## Slide 16
The P-v-T surfaces present a great deal of information at once, but in a thermodynamic analysis it is more convenient to work with two-dimensional diagrams, such as the P-v and T-v diagrams.

## Slide 17: PROPERTY TABLES
For most substances, the relationships among thermodynamic properties are too complex to be expressed by simple equations.
Therefore, properties are frequently presented in the form of tables.
Some thermodynamic properties can be measured easily, but others cannot and are calculated by using the relations between them and measurable properties.
The results of these measurements and calculations are presented in tables in a convenient format.
Enthalpy—A Combination Property
The combination u + Pv is frequently encountered in the analysis of control volumes.
The product pressure  volume has energy units.

## Slide 18: Saturated Liquid and Saturated Vapor States
Table A–4: Saturation properties of water under temperature.
Table A–5: Saturation properties of water under pressure.
A partial list of Table A–4.
Enthalpy of vaporization, hfg (Latent heat of vaporization): The amount of energy needed to vaporize a unit mass of saturated liquid at a given temperature or pressure.

## Slide 19
Examples: Saturated liquid and saturated vapor states of water on T-v and P-v diagrams.

## Slide 20: Saturated Liquid–Vapor Mixture
Quality, x : The ratio of the mass of vapor to the total mass of the mixture. Quality is between 0 and 1 0: sat. liquid, 1: sat. vapor.
The properties of the saturated liquid are the same whether it exists alone or in a mixture with saturated vapor.
The relative amounts of liquid and vapor phases in a saturated mixture are specified by the quality x.
A two-phase system can be treated as a homogeneous mixture for convenience.
Temperature and pressure are dependent properties for a mixture.

## Slide 21
y v, u, or h.

## Slide 22
Examples: Saturated liquid-vapor mixture states on T-v and P-v diagrams.

## Slide 23: Superheated Vapor
In the region to the right of the saturated vapor line and at temperatures above the critical point temperature, a substance exists as superheated vapor.
In this region, temperature and pressure are independent properties.
A partial listing of Table A–6.
At a specified P, superheated vapor exists at a higher h than the saturated vapor.
Compared to saturated vapor, superheated vapor is characterized by

## Slide 24: Compressed Liquid
Compressed liquid is characterized by
y  v, u, or h
A more accurate relation for h
A compressed liquid may be approximated as a saturated liquid at the given temperature.
The compressed liquid properties depend on temperature much more strongly than they do on pressure.

## Slide 26: Reference State and Reference Values
The values of u, h, and s cannot be measured directly, and they are calculated from measurable properties using the relations between properties.
However, those relations give the changes in properties, not the values of properties at specified states.
Therefore, we need to choose a convenient reference state and assign a value of zero for a convenient property or properties at that state.
The referance state for water is 0.01°C and for R-134a is -40°C in tables.
Some properties may have negative values as a result of the reference state chosen.
Sometimes different tables list different values for some properties at the same state as a result of using a different reference state.
However, In thermodynamics we are concerned with the changes in properties, and the reference state chosen is of no consequence in calculations.

## Slide 27: THE IDEAL-GAS EQUATION OF STATE
Equation of state: Any equation that relates the pressure, temperature, and specific volume of a substance.
The simplest and best-known equation of state for substances in the gas phase is the ideal-gas equation of state. This equation predicts the P-v-T behavior of a gas quite accurately within some properly selected region.
R: gas constant
M: molar mass (kg/kmol)
Ru: universal gas constant
Ideal gas equation of state
Different substances have different gas constants.

## Slide 28
Mass = Molar mass  Mole number
Various expressions of ideal gas equation
Ideal gas equation at two states for a fixed mass
Real gases behave as an ideal gas at low densities (i.e., low pressure, high temperature).

## Slide 29: Is Water Vapor an Ideal Gas?
At pressures below 10 kPa, water vapor can be treated as an ideal gas, regardless of its temperature, with negligible error (less than 0.1 percent).
At higher pressures, however, the ideal gas assumption yields unacceptable errors, particularly in the vicinity of the critical point and the saturated vapor line.
In air-conditioning applications, the water vapor in the air can be treated as an ideal gas. Why?
In steam power plant applications, however, the pressures involved are usually very high; therefore, ideal-gas relations should not be used.

## Slide 30: COMPRESSIBILITY FACTOR—A MEASURE OF DEVIATION FROM IDEAL-GAS BEHAVIOR
Compressibility factor Z A factor that accounts for the deviation of real gases from ideal-gas behavior at a given temperature and pressure.
The farther away Z is from unity, the more the gas deviates from ideal-gas behavior.
Gases behave as an ideal gas at low densities (i.e., low pressure, high temperature).
Question: What is the criteria for low pressure and high temperature?
Answer: The pressure or temperature of a gas is high or low relative to its critical temperature or pressure.

## Slide 31
Comparison of Z factors for various gases.
Reduced temperature
Reduced pressure
Pseudo-reduced specific volume
Z can also be determined from a knowledge of PR and vR.

## Slide 32: OTHER EQUATIONS OF STATE
Several equations have been proposed to represent the P-v-T behavior of substances accurately over a larger region with no limitations.
Van der Waals Equation of State
Critical isotherm of a pure substance has an inflection point at the critical state.
This model includes two effects not considered in the ideal-gas model: the intermolecular attraction forces and the volume occupied by the molecules themselves. The accuracy of the van der Waals equation of state is often inadequate.

## Slide 33
Beattie-Bridgeman Equation of State
The constants are given in Table 3–4 for various substances. It is known to be reasonably accurate for densities up to about 0.8cr.
Benedict-Webb-Rubin Equation of State
The constants are given in Table 3–4. This equation can handle substances at densities up to about 2.5 cr.
Virial Equation of State
The coefficients a(T), b(T), c(T), and so on, that are functions of temperature alone are called virial coefficients.

## Slide 37: Summary
Pure substance
Phases of a pure substance
Phase-change processes of pure substances
  Compressed liquid, Saturated liquid, Saturated vapor, Superheated vapor
  Saturation temperature and Saturation pressure
Property diagrams for phase change processes
  The T-v diagram, The P-v diagram, The P-T diagram, The P-v-T surface
Property tables
  Enthalpy
  Saturated liquid, saturated vapor, Saturated liquid vapor mixture, Superheated vapor, compressed liquid
  Reference state and reference values
The ideal gas equation of state
  Is water vapor an ideal gas?
Compressibility factor
Other equations of state
  van der Waals Equation of State, Beattie-Bridgeman Equation of State
  Benedict-Webb-Rubin Equation of State, Virial Equation of State